## Slide 1
Autonomous Traffic Intersection Management for Cross-Traffic Control

## Slide 2: Motivation
Urban traffic growth increases congestion, delay, and intersection conflicts.
This motivates the development of a safe, real-time, and verifiable intersection control system that ensures:
collision avoidance
improved traffic throughput
embedded real-time feasibility
Smart intersections replace traffic lights with reservation-based scheduling for conflict-free access.
Autonomous vehicles enable cooperative intersection management beyond signal-based control.
ITS and V2X enable real-time coordination between vehicles and infrastructure. Intelligent Transportation Systems Vehicle-to-Everything (V2X) Communication.
Fixed-time traffic lights are inefficient under dynamic and heterogeneous traffic conditions.
[1][2]

## Slide 3: Objectives
Model a 4-way intersection with lane-level detail
Design conflict-aware scheduling mechanism
Implement reservation-based controller
Ensure:
  collision-free executionfairness + reduced waiting time
  Model system as a cyber-physical system
  Enable:UPPAAL formal verification
  FreeRTOS embedded mapping
Notes: We can say edge deployment a sa title

## Slide 4: Requirments
[4]
Functional Core
Detect vehicle state (V2X + sensors).
Maintain intersection queue and global state.
Detect conflicts between vehicle paths.
Assign safe time-space reservations.
Control entry + execution of vehicles.
Handle emergency priority requests.
Safety Requirements
No collision in intersection zones→ mutual exclusion of Q1–Q4.
No deadlock in system→ system always progresses.
No starvation→ every vehicle eventually gets service.
Real-time bounded response→ scheduling within time limits.
Safe emergency handling→ priority without violating safety.

## Slide 5: System Architecture
Block Diagram

## Slide 6: System Workflow
Sequence Diagram

## Slide 7: Behavioral Models
FSM

## Slide 8: UPPAAL Model
System Templates
VehicleGenerator
Generates vehicle requests dynamically
Assigns movement type + activates vehicles
Vehicle (Agent Model)
Represents vehicle lifecycle
idle → request → waiting → done
Scheduler
Computes priority using aging + cost
Selects selectedVehicle
Produces scheduling decision
IntersectionController
Reserves intersection quadrants (Q1–Q4)
Executes movement safely
Releases resources after execution
Notes: Future work: EmergencyHandlerOverrides normal scheduling when needed

## Slide 9: UPPAAL Model
Scheduling policy
A reservation-based, conflict-aware scheduling policy selects vehicles for safe intersection access while ensuring fairness and real-time constraints.
Triggered when queue_len > 0
Computes: score = waitTime − cost
Selects vehicle with highest score
Output: selectedVehicle
Trade-off Dimension | Design Choice | Benefit | Limitation
Fairness vs Efficiency | Aging (waitTime) + cost-aware scoring | Prevents starvation, prioritizes waiting vehicles | May select less optimal routes
Optimality vs Real-Time | Greedy single-step selection | Bounded computation time, predictable behavior | No global optimization or future prediction
Safety vs Throughput | Strict quadrant reservation (Q1–Q4) | Collision-free execution guarantee | Limits parallel vehicle movement
Notes: Future work: EmergencyHandlerOverrides normal scheduling when needed
Achieve safe, deterministic, and real-time scheduling while balancing fairness and efficiency under strict intersection constraints.
We verify the system using CTL properties in UPPAAL to ensure safety (no collisions), liveness (progress), and real-time constraints under all possible execution traces.

## Slide 10: Verification
Objective
safe (no collisions)
live (progress guaranteed)
deadlock-free
real-time compliant
Ensure the system is:
Safety Properties
Property | Meaning
A[] not (Q1 && Q4) | No conflicting vehicles occupy same intersection space
A[] not (Q2 && Q3) | Mutual exclusion in crossing zones
A[] system_busy imply !(Q1 && Q2 && Q3 && Q4) | Intersection cannot be in invalid full-state overlap

## Slide 11: Verification
Liveness Properties (Progress)
Property | Meaning
A<> Scheduler.Propose | Scheduler eventually makes a decision
A<> IntersectionController.Execute | Vehicles eventually cross intersection
Real-Time Constraints
Property | Meaning
A[] sched_clk <= SCHED_DEADLINE | Scheduling completes within bounded time
A[] exec_clk <= SLOT_TIME | Execution is time-bounded per vehicle
Notes: UPPAAL model guarantees that every scheduling decision results in a collision-free, time-bounded, and eventually progressing execution sequence.

## Slide 12: Verification

## Slide 13
Implementation Mapping
FreeRTOS tasks mapping
VHDL FSM mapping
This is how it runs on real systems

## Slide 16: Conclusion

## Slide 17
Refereneces
[1] M. Dresner and P. Stone, “A Multiagent Approach to Autonomous Intersection Management,” Journal of Artificial Intelligence Research, 2008.
[2] H. Hartenstein and K. Laberteaux, “A Tutorial Survey on Vehicular Ad Hoc Networks,” IEEE Communications Magazine, 2008.

## Slide 18
Q & A

## Slide 19: Appendix

## Slide 20: Problem Statement
[1][2]
static signal timing → inefficient utilization
high waiting times under variable traffic load
limited adaptability to autonomous vehicles
lack of global coordination between vehicles
Traditional traffic systems suffer from:
Core Challenge
  dynamically schedules vehicles.
  ensures collision-free intersection access.
  satisfies real-time constraints.
  is implementable on embedded systems.
Project Objectives