## Slide 1
Autonomous Traffic Intersection Management
Name | Mat
Nader Yahia | 2210026
Hassan Sazid | 2220046
Mostafizur Rahman | 2219941
Umer Hayat | 1232270
Supervisors
Prof. Dr.rer.nat. Achim Rettberg
Prof.Dr.rer.nat. Stefan Henkler

## Slide 2: Motivation
FHWA, intersections cause about 45% of all urban traffic congestion.
Fixed-time traffic lights are inefficient under dynamic and heterogeneous traffic conditions.
Eco-Driving and Fuel Consumption Mitigation.
Complete Elimination of Human Driver Errors.
Drastic Reduction in Average Travel Delay.
[1]-[3]
Notes: 1-making them the main bottlenecks in city road networks.
2-Drastic Reduction in Average Travel Delay

## Slide 3: Requirements
[4]
Functional Core
Detect vehicle state (V2X + sensors).
Maintain intersection queue and global state.
Detect conflicts between vehicle paths.
Assign safe time-space reservations.
Control entry + execution of vehicles.
Handle emergency priority requests (Future work).
Safety Requirements
No collision in intersection zones→ mutual exclusion of Q1–Q4.
No deadlock in system→ system always progresses.
No starvation→ every vehicle eventually gets service.
Real-time bounded response→ scheduling within time limits.
Safe emergency handling→ priority without violating safety (Future work).

## Slide 4
Use Cases
Reservation Request
Conflict Check
Grant / Wait Decision
Src: Image Genrated by ChatGPT-5.5

## Slide 5: Intersection Trajectory
Trajectory Mapping: Groups 12 maneuvers (M1–M12) into standard straight or turning paths.
Spatial Resource Allocation: Links paths to quadrant sequences (Q1–Q4) for collision avoidance.
Conflict Identification: Flags overlapping paths (e.g., M1, M9, M10 sharing Q2,Q3) to spot bottlenecks.
Notes: Trajectory Mapping: Discretizes 12 directional maneuvers (M1 to M12) into standardized straight and turning paths.
Spatial Resource Allocation: Links each movement to specific quadrant sequences (Q1 to Q4) to establish collision-avoidance logic.
Conflict Identification: Isolates overlapping path dependencies (e.g., M1, M9, and M10 all demanding Q2 \rightarrow Q3) to highlight scheduling bottlenecks.

## Slide 6: System Architecture

## Slide 7: UPPAAL Model
Generates vehicle requests.
Assigns movement type.
Activates vehicles.
Represent vehicle lifecycle.
Toggles the activation flag.
Preserving routing data.
Vehicle (Agent Model)
VehicleGenerator
Notes: 1- A-Slot Allocation: Assigns the lowest open ID (i = 0 to 3) to the incoming vehicle.
B-State Reset: Activates the vehicle agent, maps its request, and resets its wait timer to 0. Cost Weighting: Sets cost = 1 for straight paths (M1–M4) and cost = 2 for turns.
C-Maneuver Rotation: Increments the global tracking counter, cycling from 1 to 12.
2- A-State Management: Advances the vehicle instance through a simple deterministic
B-Liveness Notification: Toggles the activation flag (vehicleActive[vid] = true) to alert the core scheduler that a vehicle occupies the queue.
C-Buffer Isolation: Stores its unique structural target in an internal variable
Future work: EmergencyHandlerOverrides normal scheduling when needed

## Slide 8: UPPAAL Model
Scheduling policy
A Reservation-based , conflict-aware scheduling policy selects vehicles for safe intersection access considering fairness and real-time constraints.
Notes: Future work: EmergencyHandler Overrides normal scheduling when needed
Achieve safe, deterministic, and real-time scheduling while balancing fairness and efficiency under strict intersection constraints.
We verify the system using CTL properties in UPPAAL to ensure safety (no collisions), liveness (progress), and real-time constraints under all possible execution traces.
Reservation-based search through queueO(N)
Fully parallel FPGA reservation engine Approximately O(1) scheduling latency
During each scheduling cycle, only the head-of-queue request is evaluated, and the FPGA performs conflict detection and reservation using fixed-size quadrant logic. Consequently, the scheduling decision has constant time complexity, O(1)O(1)O(1), independent of the number of waiting vehicles.

## Slide 9: UPPAAL Model
Intersection Controller
Notes: Future work: EmergencyHandler Overrides normal scheduling when needed
Achieve safe, deterministic, and real-time scheduling while balancing fairness and efficiency under strict intersection constraints.
We verify the system using CTL properties in UPPAAL to ensure safety (no collisions), liveness (progress), and real-time constraints under all possible execution traces.

## Slide 10: Verification
Objective
safety (no collisions).
Liveness (progress guaranteed).
Deadlock-free.
Real-time compliant.
Ensure the system is:
Safety Properties

## Slide 11: Verification

## Slide 12
System Partitioning
Notes: We can say edge deployment a sa title

## Slide 13
ARM Processor
FreeRTOS
• Scheduler
• Queue Manager
• Task Manager
• V2X Communication
• Emergency Policy
AXI / high‑speed
interconnect bus
Interrupts +
register access
FPGA Fabric
HW‑centric
• Quadrant logic Q1–Q4
• Conflict matrix
• Reservation arbiter
• SLOT_TIME FPGA timer
Hybrid
EmergencyHandler
ARM + FPGA override
Sensing / V2X
communication interfaces
Co‑design result: Flexible Scheduling + Deterministic Parallel Conflict Checking.
System Partitioning
Notes: Software Allocations:
  Movement Identification: Evolving movement tracking logic requires flexible software implementation.
  Queue Management: Dynamic data structures are easier to implement and modify.
  Scheduler & Reservation: Fairness algorithms and availability checks are easier to verify.
  Quadrant Manager: Occupancy states utilize simple, highly flexible, low-load software bitmasks.
  Diagnostics & Logging: Event tracking and statistics are naturally software-based responsibilities.
Hybrid Allocations (Controllers, Emergency, Communication)
  Division of Labor: Software decides logic and protocols; hardware drives physical outputs.

## Slide 14: FreeRTOS Realization
1. TASK DECOMPOSITION
Hierarchical execution by priority
HIGHEST PRIO
EmergencyTask — System override
void EmergencyTask(void *pvParam)
HIGH PRIO
SchedulerTask — FCFS decision
void SchedulerTask(void *pvParam)
HIGH PRIO
IntersectionManagerTask — Quadrant auth
void MonitorTask(void *pvParam)
MEDIUM PRIO
V2XReceiverTask — Ingest requests
void V2XReceiverTask(void *pvParam)
MEDIUM PRIO
FPGAInterfaceTask — Hardware sync
void FPGAInterfaceTask(void *pvParam)
2. INTER-TASK COMMUNICATION
Protecting shared spatial resources
Queues (N/S/E/W)
Buffer incoming FCFS request structures safely.
enqueue(), dequeue()
Mutexes
Ensure atomic state checks and spatial quadrant reservations.
xSemaphoreCreateMutex()
Binary Semaphores
Instantly wake scheduler task upon vehicle request arrival.
xSemaphoreCreateBinary()
Event Groups
Manage global state bitmasks (Normal vs. Emergency override).
xEventGroupCreate()
Notes: We can say edge deployment a sa title

## Slide 15: FreeRTOS Realization
Notes: We can say edge deployment a sa title

## Slide 16
FPGA Core Realization
Movement decoder converts request ID into required intersection quadrants.
Conflict detection checks if requested quadrants are already occupied.
Reservation arbiter grants access only when no conflict exists.
Slot timer automatically releases reserved quadrants after crossing.
Done signal notifies FREETROS that the request is completed.
Implemented Modules:

## Slide 17
FPGA Core Realization

## Slide 18: Conclusion
This project presented a real-time autonomous intersection controller based on a heterogeneous SoC architecture.
Safe and collision-free intersection management using quadrant reservation
Deterministic real-time behavior ensured by FPGA acceleration.
Scalable scheduling model using queue-based reservation logic .
Key Outcomes
The system combines:
  FreeRTOS (ARM): vehicle request handling, FCFS-based queue management, and emergency control
  FPGA (VHDL): deterministic reservation, conflict detection, and quadrant-based execution control
  AXI-Lite Interface: memory-mapped communication between software and hardware
Clear separation of responsibilities:
    Software = decision + scheduling
    Hardware = safety + execution enforcement

## Slide 19
Refereneces
[1] Z. Zhong, M. Nejad, and E. E. Lee, "Autonomous and Semiautonomous Intersection Management: A Survey," IEEE Intelligent Transportation Systems Magazine, vol. 13, no. 1, pp. 53–70, 2021. https://doi.org/10.1109/mits.2020.3014074Cited by: 109
[2] A. Abbas-Turki et al., "Autonomous Intersection Management: Optimal Trajectories and Efficient Scheduling," Sensors, vol. 23, no. 3, p. 1509, 2023. https://doi.org/10.3390/s23031509Cited by: 29
[3] B. Li, Y. Zhang, N. Jia, and X. Peng, "Autonomous Intersection Management over Continuous Space: A Microscopic and Precise Solution via Computational Optimal Control," IFAC-PapersOnLine, vol. 53, no. 2, pp. 17071–17076, 2020. https://doi.org/10.1016/j.ifacol.2020.12.1611Cited by: 28