## Slide 1
High-Level Synthesis
for Multi-Core Systems
Md Mostafizur Rahman
Electronic Engineering • Hochschule Hamm-Lippstadt
High-Level Synthesis for Multi-Core Systems
01
Behavioral code
C/C++
SystemC
HLS compiler
Schedule
Bind
RTL hardware
VHDL
Verilog
Notes: Introduce the topic. The talk connects HLS theory with three practical experiments: C++ scheduling, POSIX speedup, and Vivado LUT reduction.

## Slide 2
Introduction
What is HLS?
HLS automates RTL generation from high-level descriptions (C/C++, SystemC, MATLAB)
Analogous to software compilation — but for hardware
Tools: AMD Xilinx Vitis HLS, ScaleHLS, BAMBU
Multi-core HLS adds:
• PE partitioning
• Communication scheduling
• Inter-PE resource sharing
6-Stage HLS Flow
① Behavioral Compilation
② Data-Width Analysis
③ Resource Allocation
④ Operation Scheduling
⑤ Resource Binding
⑥ RTL Code Generation
High-Level Synthesis for Multi-Core Systems
02
Notes: HLS abstracts away RTL coding. The 6 stages proceed in sequence; multi-core adds PE partitioning and communication scheduling between stages 3 and 4.

## Slide 3
From Code to RTL
High-Level Synthesis for Multi-Core Systems
03
1
Behavioral code
C/C++ / SystemC / MATLAB
2
DFG construction
operations + dependencies
3
Resource allocation
choose available operators
4
Scheduling
choose control steps
5
Binding
map ops to FUs/registers
6
RTL generation
VHDL / Verilog
Multi-core extension
Partitioning
Which PE?
Communication
How data moves?
Synchronization
When values arrive?
Shared resources
How to save area?
Notes: Explain HLS as a hardware compiler. The important update in multi-core HLS is not just generating RTL; the tool must partition work, schedule communication, and decide what hardware is shared.

## Slide 4
Mathematical Foundations
Data-Flow Graph (DFG)
G = (V, E) — nodes = operations, edges = data dependencies
v₁
a×b
v₂
c×d
v₃
+
Latency dᵢ = clock cycles for hardware operator
ASAP · ALAP · Mobility
ASAP
Earliest possible control step for each operation
ALAP
Latest possible step under latency constraint λ
Mobility
tᴬᴸᴬᴾ(vᵢ) − tᴬˢᴬᴾ(vᵢ) → scheduling flexibility
Parallel Speedup
S(k) = T₁ / Tₖ
T₁ = single-core latency
Tₖ = k-core latency
Ideal: S(k) ≤ k (communication overhead reduces this)
High-Level Synthesis for Multi-Core Systems
04
y = (a×b) + (c×d)
Notes: DFG is the core data structure in HLS. ASAP/ALAP bracket when an operation can run. Low mobility = critical path. Speedup formula from Amdahl's law family.

## Slide 5
Multi-Core HLS Formal Model
π
Partition
Assign each DFG node vᵢ → PE Pⱼ
s
Schedule
Assign each node a control step ∈ ℤ⁺
β
Bind
Map each operation → functional unit FU
δ
Communicate
Schedule inter-PE data transfers
Minimise total latency Λ, chip area A, power P while satisfying communication, resource, and timing constraints.
Communication Constraint: start(consumer) ≥ finish(producer) + communication delay
Communication Constraint:
s(vⱼ) ≥ s(vᵢ) + dᵢ + δᵢⱼ
High-Level Synthesis for Multi-Core Systems
05
Notes: The multi-core HLS problem is NP-hard in general. The four decision variables interact: a bad partition forces expensive communication, degrading the schedule.

## Slide 6
Algorithm Focus: Scheduling + Binding
Scheduling and binding should not be treated as two isolated problems.
High-Level Synthesis for Multi-Core Systems
06
List-based scheduler
Ready operations
predecessors done
Priority queue
critical ops first
Available FUs
respect resources
Assign PE + step
avoid cross-PE cost
Priority function
Priority(vᵢ) = 1/mobility(vᵢ) + α₁·width(vᵢ) + α₂·|succ(vᵢ)| + PE-affinity
Low mobility = critical path. PE-affinity reduces unnecessary communication.
Binding cost
χ(yᵢ,nⱼ) = ωop + ωpath + communication term
Choose not only the cheapest operator, but also the cheapest data path.
Design trade-off
Speed
parallelism
Area
sharing
Communication
delay
Fast
Small
Low delay
Notes: Explain simply: the scheduler picks ready operations, orders them by priority, and assigns them to free hardware. The binding cost shows why the tool must think about hardware paths and communication, not only operation type.

## Slide 7
Experiment Strategy
High-Level Synthesis for Multi-Core Systems
07
1
C++ scheduling model
Shows operation → step → PE assignment
sched.cpp
2
POSIX multi-core run
Measures practical speedup and overhead
matrix_pthread.c
3
Vivado FPGA synthesis
Compares separate vs. shared datapath area
VHDL + utilization report
Together they prove
DFG scheduling maps work to PEs
Real speedup is useful but not ideal
Resource sharing can reduce FPGA LUTs
Best design balances all three
Notes: This slide is the roadmap for the evidence. Emphasize that the work is not only literature: it includes scheduler logic, Linux pthread runtime, and FPGA synthesis results.

## Slide 8
C++ List-Based Scheduler
A small 2×2 matrix multiplication DFG is scheduled onto two processing elements.
High-Level Synthesis for Multi-Core Systems
08
Observed output
Step
PE1
PE2
1
v1, v2
v3, v4
2
v5, v6
v7, v8
3
v9, v10
—
4
v11, v12
—
// 2×2 matrix multiply DFG scheduling
struct Operation {
int id, latency, step=-1, core=-1;
vector<int> preds;
};
bool predecessorsDone(op, step) {
for (int p : op.preds)
if (ops[p].step+ops[p].latency > step)
return false;
return true; }
// Greedy loop: assign ready ops to PE
for (int step=1; !allScheduled(ops); step++)
for (auto& op : ops)
if (predecessorsDone(op,step))
assign to first PE with free FU;
DFG: 2×2 matrix multiply (12 ops)
2 Processing Elements
2 Functional Units per PE
Multiplication: latency = 2 cycles
Addition: latency = 1 cycle
Notes: Show the code only briefly. The main idea is that the scheduler checks if predecessors are done, then assigns the operation to a free PE. The result demonstrates a weakness: greedy scheduling ignores where operands are stored.

## Slide 9
2×2 Example: Communication-Aware Partitioning
For the 2×2 matrix product, row-based partitioning removes inter-PE data transfers.
High-Level Synthesis for Multi-Core Systems
09
Row-based partition
P1
row 0 of C
P2
row 1 of C
{v1,v2,v3,v4,v9,v10}
{v5,v6,v7,v8,v11,v12}
δᵢⱼ = 0 for all edges
Two-core schedule
Step
P1
P2
Ideal speedup: S(2) = T₁/T₂ = 12/6 = 2.0
Step | PE1 (Row 0) | PE2 (Row 1)
1 – 2 | v1 × v2 (mult) | v5 × v6 (mult)
3 | v9 (add) | v11 (add)
4 – 5 | v3 × v4 (mult) | v7 × v8 (mult)
6 | v10 (add) | v12 (add)
Notes: This slide fixes the earlier greedy issue. By giving row 0 to PE1 and row 1 to PE2, the additions consume products from the same PE. There is no communication delay, so two cores achieve ideal speedup in this small hardware schedule.

## Slide 10
POSIX Multi-Core Simulation
// matrix_pthread.c (N=64, CLK_US=8)
void *pe_worker(void *arg) {
// Each thread = one PE
int rows = N/K;
// Row-partitioned matrix multiply
for (i=start; i<end; i++)
for (j=0; j<N; j++)
C[i][j] += A[i][k]*B[k][j];
// Simulate HW latency
usleep(rows*(MUL+ADD)*CLK_US);
}
// Measure wall-clock for K=1,2,4
double T1 = run_test(1);
double T2 = run_test(2);
double T4 = run_test(4);
S(K) = T1 / TK;
Hardware Model Mapping
pthread
Processing Element (PE)
row block
DFG partition
usleep()
hardware operator latency
pthread_join
synchronization δᵢⱼ
AMD Ryzen 7
8-core target machine
Test Configuration
N = 64 × 64 matrix
6 runs — median reported
Linux CLOCK_MONOTONIC timer
gcc -O2 -pthread
High-Level Synthesis for Multi-Core Systems
10
Notes: Each pthread models one PE. Row partitioning directly maps to DFG partitioning. usleep() models HW operator latency; pthread_join models inter-PE synchronization overhead.

## Slide 11
POSIX Results
Linux pthreads model processing elements and expose real overhead.
High-Level Synthesis for Multi-Core Systems
11
Chart: 
| K=1 | K=2 | K=4
Execution time (s) | 0.002286 | 0.001346 | 0.000992
Execution time ↓
Chart: 
| K=1 | K=2 | K=4
Measured | 1 | 1.7 | 2.31
Ideal | 1 | 2 | 4
Measured vs. ideal speedup
1.00×
K=1 (baseline)
T₁ = 0.002286 s
1.70×
K=2 (two PEs)
T₂ = 0.001346 s
2.31×
K=4 (four PEs)
T₄ = 0.000992 s
Notes: Explain the difference between theory and practice. More workers reduce runtime, but the speedup is sublinear. This supports the paper’s point that communication and synchronization overhead must be modeled.

## Slide 12
FPGA Resource-Sharing Experiment
Same interface, different internal datapath: duplicated hardware vs. shared hardware.
High-Level Synthesis for Multi-Core Systems
12
Separate datapath
×
×
+
+
+
×
mode selects output
Shared-resource design
shared_mult <= op1 * op2;
MUX
MUX
×
one multiplier reused
across modes
Chart: 
| Separate | Shared
LUTs used | 262 | 212
19.1% LUT reduction
262 → 212 LUTs, same 50 IO pins
Mode 0: y = (a×b) + (c×d) → 2 multipliers + 1 adder
Mode 1: y = (a+b) × (c+d) → 2 adders + 1 multiplier
All 6 functional units always present in the netlist
No sharing — operations use dedicated hardware
Higher area, more independent logic
Lower area, resource sharing
Notes: This is the strongest hardware evidence. The shared design keeps the same inputs and outputs but reuses hardware internally. It saves 50 LUTs, or about 19.1 percent. Connect this directly to allocation and binding.

## Slide 13
RTL Output and Practical Limits
High-Level Synthesis for Multi-Core Systems
13
Input regs
MUX tree
Functional units
Register file
FSM controller
Per-PE RTL structure
Operators + registers + MUXes + FSM control signals become VHDL/Verilog hardware.
Limitations / open challenges
Exact ILP
optimal but exponential
NoC modeling
routing adds variable delay
Heterogeneity
CPU/DSP/GPU/accelerator costs differ
Memory bottlenecks
parallel cores compete for bandwidth
Notes: Explain RTL output simply: HLS creates real hardware components and an FSM to activate them each clock cycle. Then mention practical limitations: exact optimization is hard, communication networks are complex, platforms are heterogeneous, and memory bandwidth can limit scaling.

## Slide 14
Conclusion
High-Level Synthesis for Multi-Core Systems
14
C++ scheduler
DFG operations map to logical PE mapping
POSIX threads
real multi-core speedup
Vivado synthesis
19.1% LUT reduction by sharing
Final Decision: Parallelism improves speed, but communication and resource sharing decide whether the hardware is efficient.
DFG scheduling maps operations to cycles and PEs.
Pthread experiment shows real speedup, but not ideal scaling.
Vivado experiment shows 19.1% LUT reduction from sharing.
Best HLS designs balance parallelism, communication, and area.
Notes: Use this as the final content slide. Restate the main result: HLS is not only automatic translation from C to RTL. Multi-core HLS must balance speed, communication, and area.

## Slide 15
References and Questions
.
High-Level Synthesis for Multi-Core Systems
15
[1] J. P. Elliott, Understanding Behavioral Synthesis, Kluwer, 2000.
[2] P. Coussy and A. Morawiec, High-Level Synthesis: From Algorithm to Digital Circuit, Springer, 2008.
[3] S. Gupta et al., SPARK: A Parallelizing Approach to HLS of Digital Circuits, Springer, 2004.
[4] G. De Micheli, Synthesis and Optimization of Digital Circuits, McGraw-Hill, 1994.
[5] E. Casseau and B. Le Gal, Multi-mode application-specific cores based on HLS, VLSI Journal, 2012.
[6] P. G. Paulin and J. P. Knight, Force-Directed Scheduling, IEEE TCAD, 1989.
[7] A. M. Sllame and V. Drabek, List-based scheduling for HLS, DSD, 2002.
[8] M. Stephenson et al., Bitwidth analysis, PLDI, 2000.
[9] R. Nane et al., Survey and evaluation of FPGA HLS tools, IEEE TCAD, 2016.
[10] H. Ye et al., ScaleHLS, HPCA, 2022.
Thank you
Questions?
Notes: End politely and invite questions. If asked about the main contribution, answer: the presentation connects multi-core HLS theory with original scheduler, POSIX, and Vivado synthesis experiments.